## FLEXRADIO CAT COMMAND DICTIONARY

# GENERAL INFORMATION

A CAT command consists of a prefix, a parameter list, and a terminator.  Commands fall into one of three categories:  Get (read) commands that request status information from the transceiver; Set (write) commands that change transceiver status; and Answer (response) commands that return information requested in a Get command or error codes.

A correctly executed Set command does not return an Answer command.

The terminator for all CAT commands is the semicolon (;).  CAT commands are not case sensitive.  Get and Set commands must contain the correct number of parameter characters as shown in the accompanying tables.  Most Get commands are simply the prefix followed by a termination, but there are special cases where a Get command will require parameters.

# Kenwood Compatible Commands

| AG Sets or reads the AF Gain thumbwheel control |
| --- |
| Get | AG | P1 | ; |  |  |  |  |  |  |  |
| Set | AG | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | AG | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = 0 for main transceiver, 1 for future sub receiver. P2 = 000 to 255 (scaled 0 to 100 in software). A Set value of 127 = 50 on the AF Gain thumbwheel. Also see ZZAG. |

| AI Sets or reads the Auto Information function |
| --- |
| Get | AI | ; |  |  |  |  |  |  |  |  |
| Set | AI | P1 | ; |  |  |  |  |  |  |  |
| Answer | AI | P1 | : |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 or more for On. When On, the radio will broadcast the VFO (A or B) frequency when changed. Option checkbox on the Setup/CAT tab must be checked to allow this command. |

| BD Moves the transceiver down one band |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | BD | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | BD is write-only |

| BU Moves the transceiver up one band |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | BU | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | BU is write-only |

| DN Moves VFO A down by the increment set in step size |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | DN | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | DN is write-only |

| FA Sets or reads VFO A frequency |
| --- |
| Get | FA | ; |  |  |  |  |  |  |  |  |
| Set | FA | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | FA | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = frequency in Hz (11 digits). Blank digits must be 0. Example: 14,320.150 = 00014320150. |

| FB Sets or reads VFO B frequency |
| --- |
| Get | FB | ; |  |  |  |  |  |  |  |  |
| Set | FB | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | FB | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = frequency in Hz (11 digits). Blank digits must be 0. Example: 14,320.150 = 00014320150. |

| FR Sets or reads the transceiver receive VFO |
| --- |
| Get | FR | ; |  |  |  |  |  |  |  |  |
| Set | FR | P1 | ; |  |  |  |  |  |  |  |
| Answer | FR | P1 | ; |  |  |  |  |  |  |  |
| Notes | Added for third-party compatibility. P1 = 0 since the FlexRadio VFO A is always the receive VFO. |

| FT Sets or reads the transceiver transmit VFO |
| --- |
| Get | FT | ; |  |  |  |  |  |  |  |  |
| Set | FT | P1 | ; |  |  |  |  |  |  |  |
| Answer | FT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for VFO A, 1 for VFO B. |

| FW Sets or reads the DSP receive filter width (obsolete 4/4/2007, not active) |
| --- |
| Get | FW | ; |  |  |  |  |  |  |  |  |
| Set | FW | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | FW | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | FW only accepts FlexRadio filter widths. See ZZFI for values. |

| GT Sets or reads the AGC time constant thumbwheel control |
| --- |
| Get | GT | ; |  |  |  |  |  |  |  |  |
| Set | GT | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | GT | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1: Fixed = 000, Long = 001, Slow = 002, Med = 003, 004 = Fast, 005 = Custom. |

| ID Reads the transceiver ID number |
| --- |
| Get | ID | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ID | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 defaults to 019 (TS-2000). The FlexRadio id code (900) may be selected remotely using ZZID. ID is read-only. |

| IF Reads the transceiver status |
| --- |
| Get | IF | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | IF | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  | P1 | P1 | P2 | P2 | P2 | P2 | P3 | P3 | P3 | P3 |
|  | P3 | P3 | P4 | P5 | P6 | P7 | P7 | P8 | P9 | P10 |
|  | P11 | P12 | P13 | P14 | P14 | P15 | ; |  |  |  |
| Notes | P1 (11 characters) VFO A frequency in Hz. Same as FA; P2 (4 characters) Frequency step size expressed in powers of 10 (see ZZST). P3 (6 characters) RIT/XIT frequency (+nnnnn or –nnnnn). P4 (1 character) RIT status. 0 = off, 1 = on. P5 (1 character) XIT status. 0 = off, 1 = on. P6 (1 character) Channel bank number. Not used, defaulted to 0. P7 (2 characters) Channel bank number. Not used, defaulted to 00. P8 (1 character) MOX button status. 0 = off, 1 = on (transmitting). P9 (1 character) Operating mode. See MD for settings. P10 (1 character) VFO Split status. Same as FR (always 0). P11 (1 character) Scan status. Not implemented, defaulted to 0. P12 (1 character) VFO Split status. Same as FT. P13 (1 character) CTCSS tone. Not used, defaulted to 0. P14 (2 characters) More tone controls. Not used, defaulted to 00. P15 (1 character) Shift status. Not used, defaulted to 0. P9 will return a space if a non-Kenwood mode is selected on the FlexRadio. |

| KS Sets or reads CWX CW speed |
| --- |
| Get | KS | ; |  |  |  |  |  |  |  |  |
| Set | KS | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | KS | P1 | P1 | P1 | l |  |  |  |  |  |
| Notes | P1 010 – 060 in WPM |

| KY Sends text to CWX for conversion to Morse |
| --- |
| Get | KY | ; |  |  |  |  |  |  |  |  |
| Set | KY | P1 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | KY | P1 | ; |  |  |  |  |  |  |  |
| Notes | Get: P1 0 = Character buffer available, 1 = Character buffer not available (> 72 characters in the buffer). Set: P1 = space, P2 up to 24 ASCII printing characters. Empty character positions in P2 must contain a space. |

| MD Sets or reads the transceiver operating mode |
| --- |
| Get | MD | ; |  |  |  |  |  |  |  |  |
| Set | MD | P1 | ; |  |  |  |  |  |  |  |
| Answer | MD | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 values: 1 = LSB 2 = USB 3 = CWU 4 = FMN 5 = AM 6 = RTTY (DIGL) 7 = CWL 9 = FSK-R (DIGU) |

| MG Sets or reads the Microphone Gain thumbwheel control |
| --- |
| Get | MG | ; |  |  |  |  |  |  |  |  |
| Set | MG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | MG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 100. |

| MO Sets or reads the Monitor (MON) status |
| --- |
| Get | MO | ; |  |  |  |  |  |  |  |  |
| Set | MO | P1 | ; |  |  |  |  |  |  |  |
| Answer | MO | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

| NB Sets or reads the Noise Blanker 1 (NB1) status |
| --- |
| Get | NB | ; |  |  |  |  |  |  |  |  |
| Set | NB | P1 | ; |  |  |  |  |  |  |  |
| Answer | NB | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

| NT Sets or reads the Automatic Notch Filter (ANF) status |
| --- |
| Get | NT | ; |  |  |  |  |  |  |  |  |
| Set | NT | P1 | ; |  |  |  |  |  |  |  |
| Answer | NT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

| PC Sets or reads the PA Power (PWR) status |
| --- |
| Get | PC | ; |  |  |  |  |  |  |  |  |
| Set | PC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | PC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 100. |

| PR Sets or reads the Speech Compressor (COMP) status OBSOLETE 2/15/2008 |
| --- |
| Get | PR | ; |  |  |  |  |  |  |  |  |
| Set | PR | P1 | ; |  |  |  |  |  |  |  |
| Answer | PR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

| PS Sets or reads the Power Button status |
| --- |
| Get | PS | ; |  |  |  |  |  |  |  |  |
| Set | PS | P1 | ; |  |  |  |  |  |  |  |
| Answer | PS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Standby, 1 = On. |

| QI Sets the Quick Save memory (QS) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | QI | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | QI is write-only. |

| RC Clears the RIT frequency (RIT[0]) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | RC | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | RC is write-only. |

| RD Decrements the RIT Frequency |
| --- |
| Get | RD | ; |  |  |  |  |  |  |  |  |
| Set | RD | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | RD without parameters decrements the RIT frequency by 10 hz in CW and 50 hz in SSB. P1 (00000 – 99999) will set the RIT Frequency (also see ZZRF). Answer is always blank or an error message. |

| RT Sets or reads the RIT button status |
| --- |
| Get | RT | ; |  |  |  |  |  |  |  |  |
| Set | RT | P1 | ; |  |  |  |  |  |  |  |
| Answer | RT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

| RU Increments the RIT Frequency |
| --- |
| Get | RU | ; |  |  |  |  |  |  |  |  |
| Set | RU | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | RD without parameters increments the RIT frequency by 10 hz in CW and 50 hz in SSB. P1 (00000 – 99999) will set the RIT Frequency (also see ZZRF). Answer is always blank or an error message. |

| RX Sets the transceiver to Receive mode (MOX off) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | RX | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | RX is write-only. |

| SH Sets or reads the variable DSP Filter high frequency |
| --- |
| Get | SH | ; |  |  |  |  |  |  |  |  |
| Set | SH | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | SH | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | SSB Modes (USB, LSB, CWU and CWL) in Hz = 1400 = 1600 = 1800 = 2000 = 2200 = 2400 = 2600 = 2800 = 3000 = 3400 = 4000 = 5000 DSB Modes (AM, DSB, FMN, DRM, SAM) = 2500 = 3000 = 4000 = 5000 SH has no effect in RTTY, PSK, or SPEC. |

| SL Sets or reads the variable DSP filter low frequency |
| --- |
| Get | SL | ; |  |  |  |  |  |  |  |  |
| Set | SL | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | SL | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | SSB Modes (USB, LSB, CWU and CWL) in Hz = 0 = 50 = 100 = 200 = 300 = 400 = 500 = 600 = 700 = 800 = 900 = 1000 DSB Modes (AM, DSB, FMN, DRM, SAM) = 0 = 100 = 200 = 500 SL has no effect in RTTY, PSK, or SPEC. |

| SM Reads the S-Meter |
| --- |
| Get | SM | P1 | ; |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | SM | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = 0 for main transceiver. P2 = 0000 to 0030 where 0015 = S9. Current code needs improvement for readings above S9. SM is read-only. |

| SQ Sets or reads the Squelch (SQL) thumbwheel control |
| --- |
| Get | SQ | P1 | ; |  |  |  |  |  |  |  |
| Set | SQ | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | SQ | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = 0 for main transceiver. P2 = 000 to 255 (scaled in software to 0 – 160, SQ0127; = 80 on the control. |

| TX Sets the transceiver to Transmit mode (MOX on) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | TX | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | TX is write-only. Not totally compatible with Kenwood but is modified to maintain compatibility with third-party software. |

| UP Moves VFO A up by the increment set in step size |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | UP | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | UP is write-only |

| XT Sets or reads the XIT status |
| --- |
| Get | XT | ; |  |  |  |  |  |  |  |  |
| Set | XT | P1 | ; |  |  |  |  |  |  |  |
| Answer | XT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for on, 1 for off. |

FlexRadio Custom Commands

| ZZAG Sets or reads the Audio Gain control |
| --- |
| Get | ZZAG | ; |  |  |  |  |  |  |  |  |
| Set | ZZAG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZAG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 100. |

| ZZAI Sets or reads the Auto Information function |
| --- |
| Get | ZZAI | ; |  |  |  |  |  |  |  |  |
| Set | ZZAI | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZAI | P1 | : |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 or more for On. When On, the radio will broadcast the VFO (A or B) frequency when changed. Option checkbox on the Setup/CAT tab must be checked to allow this command. |

| ZZAR Sets or reads the AGC Threshold control |
| --- |
| Get | ZZAR | ; |  |  |  |  |  |  |  |  |
| Set | ZZAR | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZAR | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = -20 to +120 (Must have + or – sign). |

| ZZBD Moves the band switch down one band |
| --- |
| Set | ZZBD | ; |  |  |  |  |  |  |  |  |
| Notes | ZZBD is write-only |

| ZZBG Sets or reads the Band Group (HF/VHF) |
| --- |
| Get | ZZBG | ; |  |  |  |  |  |  |  |  |
| Set | ZZBG | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZBG | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for HF, 1 for VHF. |

| ZZBI Sets or reads the Binaural (BIN) status |
| --- |
| Get | ZZBI | ; |  |  |  |  |  |  |  |  |
| Set | ZZBI | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZBI | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZBR Sets or reads the BCI Rejection button status |
| --- |
| Get | ZZBR | ; |  |  |  |  |  |  |  |  |
| Set | ZZBR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZBR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZBS Sets or reads the Band Switch |
| --- |
| Get | ZZBS | ; |  |  |  |  |  |  |  |  |
| Set | ZZBS | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZBS | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | HF P1 values: 160, 080, 060, 040, 030, 020, 017, 015, 012, 010, 006, 002 (when 2 meter transverter is installed), 888 (GEN), and 999 (WWV). VHF P1 values: V001 thru V013. |

| ZZBU Moves the band switch up one band |
| --- |
| Set | ZZBU | ; |  |  |  |  |  |  |  |  |
| Notes | ZZBU is write-only |

| ZZBY Closes the console |
| --- |
| Set | ZZBY | ; |  |  |  |  |  |  |  |  |
| Notes | ZZBU is write-only |

| ZZCB Sets or reads the Break In Enable checkbox status |
| --- |
| Get | ZZCB | ; |  |  |  |  |  |  |  |  |
| Set | ZZCB | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZCB | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZCD Sets or reads the Break In Delay value |
| --- |
| Get | ZZCD | ; |  |  |  |  |  |  |  |  |
| Set | ZZCD | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZCD | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 0150 to 5000 |

| ZZCF Sets or reads the Show TX CW Frequency checkbox status |
| --- |
| Get | ZZCF | ; |  |  |  |  |  |  |  |  |
| Set | ZZCF | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZCF | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZCI Sets or reads the CW Iambic checkbox status |
| --- |
| Get | ZZCI | ; |  |  |  |  |  |  |  |  |
| Set | ZZCI | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZCI | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZCL Sets or reads the CW Pitch (Setup ¦ DSP) |
| --- |
| Get | ZZCL | ; |  |  |  |  |  |  |  |  |
| Set | ZZCL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZCL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 0200 to 1200. |

| ZZCM Sets or reads the CW Monitor checkbox status |
| --- |
| Get | ZZCM | ; |  |  |  |  |  |  |  |  |
| Set | ZZCM | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZCM | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZCP Sets or reads the Compander (CMP) button status |
| --- |
| Get | ZZCP | ; |  |  |  |  |  |  |  |  |
| Set | ZZCP | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZCP | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZCS Sets or reads the CW Speed |
| --- |
| Get | ZZCS | ; |  |  |  |  |  |  |  |  |
| Set | ZZCS | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZCS | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = 01 to 60 |

| ZZCT Sets or reads the Compander Threshold value |
| --- |
| Get | ZZCT | ; |  |  |  |  |  |  |  |  |
| Set | ZZCT | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZCT | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = 00 to 10. |

| ZZCU Reads the CPU Usage |
| --- |
| Get | ZZCU | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZCU | P1 | P1 | P1 | P1 | P1 | P1 | ; |  |  |
| Notes | P1 = 000.00 to 100.00 |

| ZZDA Sets or reads the Display Average (AVG) status |
| --- |
| Get | ZZDA | ; |  |  |  |  |  |  |  |  |
| Set | ZZDA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZDA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZDM Sets or reads the Display Mode |
| --- |
| Get | ZZDM | ; |  |  |  |  |  |  |  |  |
| Set | ZZDM | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZDM | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 values: 0 = Spectrum 1 = Panadapter 2 = Scope 3 = Phase 4 = Phase2 5 = Waterfall 6 = Histogram 7 = Off |

| ZZDX Sets or reads the Phone DX button status |
| --- |
| Get | ZZDX | ; |  |  |  |  |  |  |  |  |
| Set | ZZDX | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZDX | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZEA Sets or reads the RX EQ values |
| --- |
| Get | ZZEA | ; |  |  |  |  |  |  |  |  |
| Set | ZZEA | P1 | P1 | P1 | P2 | P2 | P2 | P3 | P3 | P3 |
|  |  | P4 | P4 | P4 | P5 | P5 | P5 | P6 | P6 | P6 |
|  |  | P7 | P7 | P7 | P8 | P8 | P8 | P9 | P9 | P9 |
|  |  | P10 | P10 | P10 | P11 | P11 | P11 | P12 | P12 | P12 |
|  |  | ; |  |  |  |  |  |  |  |  |
| Answer | ZZEA | P1 | P1 | P1 | P2 | P2 | P2 | P3 | P3 | P3 |
|  |  | P4 | P4 | P4 | P5 | P5 | P5 | P6 | P6 | P6 |
|  |  | P7 | P7 | P7 | P8 | P8 | P8 | P9 | P9 | P9 |
|  |  | P10 | P10 | P10 | P11 | P11 | P11 | P12 | P12 | P12 |
|  |  | ; |  |  |  |  |  |  |  |  |
| Notes | P1 = number of EQ bands (003 or 010); P2 = EQ preamp setting (-12 to 015); P3 thru P12 are the setting of each EQ band (-12 to 015). If the number of bands = 003, P6 thru P12 are all zeros. |

| ZZEB Sets or reads theTX EQ values |
| --- |
| Get | ZZEA | ; |  |  |  |  |  |  |  |  |
| Set | ZZEA | P1 | P1 | P1 | P2 | P2 | P2 | P3 | P3 | P3 |
|  |  | P4 | P4 | P4 | P5 | P5 | P5 | P6 | P6 | P6 |
|  |  | P7 | P7 | P7 | P8 | P8 | P8 | P9 | P9 | P9 |
|  |  | P10 | P10 | P10 | P11 | P11 | P11 | P12 | P12 | P12 |
|  |  | ; |  |  |  |  |  |  |  |  |
| Answer | ZZEA | P1 | P1 | P1 | P2 | P2 | P2 | P3 | P3 | P3 |
|  |  | P4 | P4 | P4 | P5 | P5 | P5 | P6 | P6 | P6 |
|  |  | P7 | P7 | P7 | P8 | P8 | P8 | P9 | P9 | P9 |
|  |  | P10 | P10 | P10 | P11 | P11 | P11 | P12 | P12 | P12 |
|  |  | ; |  |  |  |  |  |  |  |  |
| Notes | P1 = number of EQ bands (003 or 010); P2 = EQ preamp setting (-12 to 015); P3 thru P12 are the setting of each EQ band (-12 to 015). If the number of bands = 003, P6 thru P12 are all zeros. |

| ZZER Sets or reads the RX EQ button status |
| --- |
| Get | ZZER | ; |  |  |  |  |  |  |  |  |
| Set | ZZER | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZER | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = OFF, 1 = ON |

| ZZET Sets or reads the TX EQ button status |
| --- |
| Get | ZZET | ; |  |  |  |  |  |  |  |  |
| Set | ZZET | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZET | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = OFF, 1 = ON |

| ZZFA Sets or reads VFO A frequency |
| --- |
| Get | ZZFA | ; |  |  |  |  |  |  |  |  |
| Set | ZZFA | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZFA | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = frequency in Hz (11 digits). Blank digits must be 0. Example: 14,320.150 = 00014320150. |

| ZZFB Sets or reads VFO B frequency |
| --- |
| Get | ZZFB | ; |  |  |  |  |  |  |  |  |
| Set | ZZFB | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZFB | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = frequency in Hz (11 digits). Blank digits must be 0. Example: 14,320.150 = 00014320150. |

| ZZFH Sets or reads DSP Filter High |
| --- |
| Get | ZZFH | ; |  |  |  |  |  |  |  |  |
| Set | ZZFH | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer | ZZFH | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Notes | P1 = frequency in Hz -9999 to 09999. |

| ZZFI Sets or reads the current DSP receive filter |
| --- |
| Get | ZZFI | ; |  |  |  |  |  |  |  |  |
| Set | ZZFI | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZFI | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 values: lsb/usb/digl/digu am/fmn/sam/dsb cwl/cwu 00 5.0K 16K 1.0K 01 4.4K 12K 800 02 3.8K 10K 750 03 3.3K 8.0K 600 04 2.9K 6.6K 500 05 2.7K 5.2K 400 06 2.4K 4.0K 250 07 2.1K 3.1K 100 08 1.8K 2.9K 50 09 1.0K 2.4K 25 10 VAR1 VAR1 VAR1 11 VAR2 VAR2 VAR2 These are the default values for the receive filters. If you customize your filters, your custom values will be displayed. |

| ZZFL Sets or reads DSP Filter Low |
| --- |
| Get | ZZFL | ; |  |  |  |  |  |  |  |  |
| Set | ZZFL | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer | ZZFL | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Notes | P1 = frequency in Hz -9999 to 09999. |

| ZZFM Reads the FlexRadio Model Number |
| --- |
| Get | ZZFM | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZFM | P1 | ; |  |  |  |  |  |  |  |
| Notes | Read only. P1: 0 = SDR1000, 1 = FLEX5000. |

| ZZFV Reads single data byte FlexWire data |
| --- |
| Get | ZZFV | P1 | P1 | P2 | P2 | ; |  |  |  |  |
|  | Write only. P1 = 00 – FF , address P2 = 00 – FF, data Case insensitive. Address is returned with data: ZZFV95: returns ZZFV95xx where xx is the data. |

| ZZFW Reads double data byte FlexWire data |
| --- |
| Get | ZZFW | P1 | P1 | P2 | P2 | P3 | P3 | ; |  |  |
| Notes | Write only. P1 = 00 – FF, address P2 = 00 – FF, data byte 1 P3 = 00 – FF, data byte 2 Case insensitive. Address is returned with data: ZZFW95 returns ZZFW95xxxx; where xxxx is the data. |

| ZZFX Sends single data byte FlexWire command |
| --- |
| Set | ZZFX | P1 | P1 | P2 | P2 | ; |  |  |  |  |
|  | Write only. P1 = 00 – FF , address P2 = 00 – FF, data Case insensitive |

| ZZFY Sends double data byte FlexWire command |
| --- |
| Set | ZZFY | P1 | P1 | P2 | P2 | P3 | P3 | ; |  |  |
| Notes | Write only. P1 = 00 – FF, address P2 = 00 – FF, data byte 1 P3 = 00 – FF, data byte 2 Case insensitive |

| ZZGE Sets or reads the Noise Gate Enable button status |
| --- |
| Get | ZZGE | ; |  |  |  |  |  |  |  |  |
| Set | ZZGE | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZGE | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZGL Sets or reads the Noise Gate Threshold value |
| --- |
| Get | ZZGL | ; |  |  |  |  |  |  |  |  |
| Set | ZZGL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZGL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = -160 to 0 (- sign required except for 0000). |

| ZZGT Sets or reads the AGC thumbwheel control |
| --- |
| Get | ZZGT | ; |  |  |  |  |  |  |  |  |
| Set | ZZGT | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZGT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 values: 0 = Fixed 1 = Long 2 = Slow 3 = Med 4 = Fast 5 = Custom |

| ZZHA Sets or reads Audio Buffer Size |
| --- |
| Get | ZZHA | ; |  |  |  |  |  |  |  |  |
| Set | ZZHA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHR Sets or reads DSP RX Buffer Phone Size |
| --- |
| Get | ZZHR | ; |  |  |  |  |  |  |  |  |
| Set | ZZHR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHT Sets or reads DSP TX Buffer Phone Size |
| --- |
| Get | ZZHT | ; |  |  |  |  |  |  |  |  |
| Set | ZZHT | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHU Sets or reads DSP RX Buffer CW Size |
| --- |
| Get | ZZHU | ; |  |  |  |  |  |  |  |  |
| Set | ZZHU | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHU | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHV Sets or reads DSP TX Buffer CW Size |
| --- |
| Get | ZZHV | ; |  |  |  |  |  |  |  |  |
| Set | ZZHV | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHV | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHW Sets or reads DSP TX Buffer Digital Size |
| --- |
| Get | ZZHW | ; |  |  |  |  |  |  |  |  |
| Set | ZZHW | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHW | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZHX Sets or reads DSP TX Buffer Digital Size |
| --- |
| Get | ZZHX | ; |  |  |  |  |  |  |  |  |
| Set | ZZHX | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZHX | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 256, 1 = 512, 2 = 1024, 3 = 2048, 4 = 4096 |

| ZZID Sets the transceiver identification to FlexRadio |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | ZZID | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | ZZID is used to remotely force the transceiver id to 900 FlexRadio). |

| ZZIF Reads the FlexRadio status |
| --- |
| Get | ZZIF | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZIF | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  | P1 | P1 | P2 | P2 | P2 | P2 | P3 | P3 | P3 | P3 |
|  | P3 | P3 | P4 | P5 | P6 | P7 | P7 | P8 | P9 | P9 |
|  | P10 | P11 | P12 | P13 | P14 | P14 | P15 | ; |  |  |
| Notes | P1 (11 characters) VFO A frequency in Hz. Same as FA; P2 (4 characters) Frequency step size expressed in powers of 10 (see ZZST). P3 (6 characters) RIT/XIT frequency (+nnnnn or –nnnnn). P4 (1 character) RIT status. 0 = off, 1 = on. P5 (1 character) XIT status. 0 = off, 1 = on. P6 (1 character) Channel bank number. Not used, defaulted to 0. P7 (2 characters) Channel bank number. Not used, defaulted to 00. P8 (1 character) MOX button status. 0 = off, 1 = on (transmitting). P9 (2 character) Operating mode. See ZZMD for settings. P10 (1 character) VFO Split status. Same as FR (always 0). P11 (1 character) Scan status. Not implemented, defaulted to 0. P12 (1 character) VFO Split status. Same as ZZSP. P13 (1 character) CTCSS tone. Not used, defaulted to 0. P14 (2 characters) More tone controls. Not used, defaulted to 00. P15 (1 character) Shift status. Not used, defaulted to 0. |

| ZZIS Sets or reads the variable filter width slider |
| --- |
| Get | ZZIS | ; |  |  |  |  |  |  |  |  |
| Set | ZZIS | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer | ZZIS | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Notes | P1 = 00000 to 10000. |

| ZZIT Sets or reads the variable filter shift slider |
| --- |
| Get | ZZIT | ; |  |  |  |  |  |  |  |  |
| Set | ZZIT | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZIT | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = “+” or “-“ P2 = 0000 to 1000 (-1000 to +1000) |

| ZZIU Resets the variable filter shift slider |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | ZZIU | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  | ; |  |  |  |
| Notes | Write only |

| ZZKS Sets or reads the CWX CW speed |
| --- |
| Get | ZZKS | ; |  |  |  |  |  |  |  |  |
| Set | ZZKS | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZKS | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 010 to 060 in WPM |

| ZZKY Sends text to CWX for conversion to Morse |
| --- |
| Get | ZZKY | ; |  |  |  |  |  |  |  |  |
| Set | ZZKY | P1 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZKY | P1 | ; |  |  |  |  |  |  |  |
| Notes | Get: P1 0 = Character buffer available, 1 = Character buffer not available (>72 characters left in buffer), 2 = buffer is empty and all code has been sent. Set: P1 = space, P2 up to 24 ASCII printing characters. . Empty character positions in P2 must contain a space. |

| ZZMA Sets or reads the Mute (MUT) status |
| --- |
| Get | ZZMA | ; |  |  |  |  |  |  |  |  |
| Set | ZZMA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZMA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZMD Sets or reads the Operating Mode |
| --- |
| Get | ZZMD | ; |  |  |  |  |  |  |  |  |
| Set | ZZMD | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZMD | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 values: 00 = LSB 01 = USB 02 = DSB 03 = CWL 04 = CWU 05 = FMN 06 = AM 07 = DIGU 08 = SPEC 09 = DIGL 10 = SAM 11 = DRM |

| ZZMG Sets or reads the Mic gain |
| --- |
| Get | ZZMG | ; |  |  |  |  |  |  |  |  |
| Set | ZZMG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZMG | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 070 |

| ZZMN Reads the DSP Filter names and values |
| --- |
| Get | ZZMN | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZMN | See below |  |  |  |  |  |  |  |  |
| Notes | P1 Values: The two-digit mode code (See ZZMD) The return string is 180 characters long, 12 groups of 15 characters each representing all the names and high/low values for each filter contained in the mode requested. The 15 character groups are broken down into subgroups of five characters: 1-5 are is name of the filter button, 6-10 is the high filter value, and 11-15 is the low filter value. Example: 5.0k 5150 –160 4.8k 4950 –160…; |

| ZZMO Sets or reads the Monitor (MON) status |
| --- |
| Get | ZZMO | ; |  |  |  |  |  |  |  |  |
| Set | ZZMO | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZMO | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = OFF, 1 = ON |

| ZZMR Sets or reads the RX Meter mode |
| --- |
| Get | ZZMR | ; |  |  |  |  |  |  |  |  |
| Set | ZZMR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZMR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = Signal Strength 1 = Signal Average 2 = ADC L 3 = ADC R 4 = Off |

| ZZMS Sets or reads the MultiRX Swap checkbox |
| --- |
| Get | ZZMS | ; |  |  |  |  |  |  |  |  |
| Set | ZZMS | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZMS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = OFF, 1 = ON |

| ZZMT Sets or reads the TX Meter mode |
| --- |
| Get | ZZMT | ; |  |  |  |  |  |  |  |  |
| Set | ZZMT | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZMT | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 Values: 00 = Forward Power 01 = Reverse Power 02 = Mic 03 = EQ 04 = Leveler 05 = Lev Gain 06 = COMP 07 = CPDR 08 = ALC 09 = ALC COMP 10 = SWR 11 = Off |

| ZZMU Sets or reads the MultiRX button status |
| --- |
| Get | ZZMU | ; |  |  |  |  |  |  |  |  |
| Set | ZZMU | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZMU | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = OFF, 1 = ON |

| ZZNA Sets or reads the Noise Blanker (NB) status |
| --- |
| Get | ZZNA | ; |  |  |  |  |  |  |  |  |
| Set | ZZNA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZNA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZNB Sets or reads the Noise Blanker 2 (NB2) status |
| --- |
| Get | ZZNB | ; |  |  |  |  |  |  |  |  |
| Set | ZZNB | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZNB | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZNL Sets or reads the Noise Blanker 1 threshold (Setup DSP tab) |
| --- |
| Get | ZZNL | ; |  |  |  |  |  |  |  |  |
| Set | ZZNL | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZNL | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 001 to 200. |

| ZZNM Sets or reads the Noise Blanker 2 threshold |
| --- |
| Get | ZZNM | ; |  |  |  |  |  |  |  |  |
| Set | ZZNM | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZNM | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 0001 to 1000. |

| ZZNR Sets or reads the Noise Reduction (NR) status |
| --- |
| Get | ZZNR | ; |  |  |  |  |  |  |  |  |
| Set | ZZNR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZNR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZNT Sets or reads the Auto Notch Filter (ANF) status |
| --- |
| Get | ZZNT | ; |  |  |  |  |  |  |  |  |
| Set | ZZNT | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZNT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZOA Sets or reads the antenna connected to RX1 (FLEX5000 only) |
| --- |
| Get | ZZOA | ; |  |  |  |  |  |  |  |  |
| Set | ZZOA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZ0A | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = N/C, 1 = Ant1, 2 = Ant2, 3 = Ant3, 4 = RX1 In. |

| ZZOB Sets or reads the antenna connected to RX2 (FLEX5000 only) |
| --- |
| Get | ZZOB | ; |  |  |  |  |  |  |  |  |
| Set | ZZOB | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZ0B | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = N/C, 1 = Ant1, 5 = RX2In, 6 = RX1Tap |

| ZZOC Sets or reads the antenna connected to the transmitter (FLEX5000 only) |
| --- |
| Get | ZZOC | ; |  |  |  |  |  |  |  |  |
| Set | ZZOC | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZ0C | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 1 = Ant1, 2 = Ant2, 3 = Ant3. |

| ZZOD Sets or reads the current antenna mode (FLEX5000 only) |
| --- |
| Get | ZZOD | ; |  |  |  |  |  |  |  |  |
| Set | ZZOD | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZ0D | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = Simple, 1 = Complex |

| ZZOE Sets or reads the RX1 loop (FLEX5000 only) |
| --- |
| Get | ZZOE | ; |  |  |  |  |  |  |  |  |
| Set | ZZOE | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZ0E | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = Loop Disabled, 1 = Loop Enabled |

| ZZOF Sets or reads the TX relays energized on transmit (FLEX5000 only) |
| --- |
| Get | ZZOF | ; |  |  |  |  |  |  |  |  |
| Set | ZZOF | P1 | P2 | P3 | ; |  |  |  |  |  |
| Answer | ZZ0F | P1 | P2 | P3 | ; |  |  |  |  |  |
| Notes | P1 = RCATX1, P2 = RCATX2, P3 = RCATX3. 1 = Enabled, 0 = Disabled, all positions must be represented: ZZOF010 = TX2 enabled, TX1 and TX2 disabled. ZZOF111 = all enabled, ZZOF000 = all disabled. |

| ZZOG Sets or reads the TX relay delays enabled on transmit (FLEX5000 only) |
| --- |
| Get | ZZOG | ; |  |  |  |  |  |  |  |  |
| Set | ZZOG | P1 | P2 | P3 | ; |  |  |  |  |  |
| Answer | ZZ0G | P1 | P2 | P3 | ; |  |  |  |  |  |
| Notes | P1 = TX1, P2 = TX2, P3 = TX3. 1 = Enabled, 0 = Disabled, all positions must be represented: ZZOG010 = TX2 enabled, TX1 and TX2 disabled. ZZOG111 = all enabled, ZZOG000 = all disabled. |

| ZZOH Sets or reads the TX relay delay times (FLEX5000 only) |
| --- |
| Get | ZZOH | P1 | ; |  |  |  |  |  |  |  |
| Set | ZZOH | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZ0H | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = TX relay number, P2 = delay in milliseconds. Example: ZZOH20100 Sets relay 2 to 100 ms. Delay range must be 0000 to 9999. |

| ZZOJ Sets or reads the Antenna Lock Checkbox |
| --- |
| Get | ZZOJ | ; |  |  |  |  |  |  |  |  |
| Set | ZZOJ | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZOJ | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZPA Sets or reads the Preamplifier (Preamp) setting |
| --- |
| Get | ZZPA | ; |  |  |  |  |  |  |  |  |
| Set | ZZPA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZPA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 values; SDR-1000 FLEX5000x FLEX3000 0 = Off 0 = Off 0 = Attn 1 = Low 1 = On 1 = Off 2 = Med 2 = Pre 3 = High |

| ZZPC Sets or reads the PA Drive level |
| --- |
| Get | ZZPC | ; |  |  |  |  |  |  |  |  |
| Set | ZZPC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZPC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 100 |

| ZZPD Sets the Display Pan Center button |
| --- |
| Set | ZZPD | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZPO Sets or reads the Display Peak button |
| --- |
| Get | ZZPO | ; |  |  |  |  |  |  |  |  |
| Set | ZZPO | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZPO | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZPS Sets or reads the Start button |
| --- |
| Get | ZZPS | ; |  |  |  |  |  |  |  |  |
| Set | ZZPS | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZPS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZPZ Sets or reads the Display Zoom buttons |
| --- |
| Get | ZZPZ | ; |  |  |  |  |  |  |  |  |
| Set | ZZPZ | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZPZ | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = 0.5X, 1 = 1X, 2 = 2X, 3 = 4X |

| ZZQM Reads the Quick Save Memory value |
| --- |
| Get | ZZQM | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZQM | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 | P1 |
|  |  | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = frequency in Hz (11 digits). Example: 14,320.150 = 00014320150. |

| ZZQR Restores the Quick Save Memory (QR) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | ZZQR | ; |  |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | ZZQR is write-only |

| ZZQS Saves VFO A frequency to Quick Memory |
| --- |
| Set | ZZQR | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZRA Sets or reads the RTTY Offset Enable VFO A status |
| --- |
| Get | ZZRA | ; |  |  |  |  |  |  |  |  |
| Set | ZZRA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZRA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZRB Sets or reads the RTTY Offset Enable VFO B status |
| --- |
| Get | ZZRB | ; |  |  |  |  |  |  |  |  |
| Set | ZZRB | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZRB | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZRC Clears the RIT frequency |
| --- |
| Set | ZZRC | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |
| ZZRD Decrements the RIT Frequency |
| Get | ZZRD | ; |  |  |  |  |  |  |  |  |
| Set | ZZRD | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | ZZRD without parameters decrements the RIT frequency by 10 hz in CW and 50 hz in SSB. P1 (00000 – 99999) will set the RIT Frequency (also see ZZRF). Answer is always blank or an error message. |

| ZZRF Sets or reads the RIT frequency |
| --- |
| Get | ZZRF; |  |  |  |  |  |  |  |  |  |
| Set | ZZRF | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZRF | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = frequency in Hz. |

| ZZRH Sets or reads the RTTY DIGH Offset Frequency |
| --- |
| Get | ZZRH; |  |  |  |  |  |  |  |  |  |
| Set | ZZRH | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZRH | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = frequency in Hz. |

| ZZRL Sets or reads the RTTY DIGL Offset Frequency |
| --- |
| Get | ZZRL; |  |  |  |  |  |  |  |  |  |
| Set | ZZRL | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZRL | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = frequency in Hz. |

| ZZRM Reads the Console meter values |
| --- |
| Get | ZZRM | P1 | ; |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZRM | P1 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 | P2 |
|  | P2 | P2 | ; |  |  |  |  |  |  |  |
| Notes | P1 Values: 0 = Signal Strength 1 = Average Strength 2 = ADC_L 3 = ADC_R 4 = ALC 5 = Forward Power 6 = Peak Power 7 = Reverse Power 8 = SWR P2 is padded left with spaces. ZZRM is read-only. |
| ***** | Developers: P1 0-3 are functional, balance needs rewrite for new meter functions in the transmit mode. |

| ZZRS Sets or reads the RX2 enable button status |
| --- |
| Get | ZZRS | ; |  |  |  |  |  |  |  |  |
| Set | ZZRS | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZRS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZRT Sets or reads the RIT enable button status |
| --- |
| Get | ZZRT | ; |  |  |  |  |  |  |  |  |
| Set | ZZRT | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZRT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for Off, 1 for On |

| ZZRU Increments the RIT Frequency |
| --- |
| Get | ZZRU | ; |  |  |  |  |  |  |  |  |
| Set | ZZRU | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | ZZRU without parameters increments the RIT frequency by 10 hz in CW and 50 hz in SSB. P1 (00000 – 99999) will set the RIT Frequency (also see ZZRF). Answer is always blank or an error message. |

| ZZRV Reads the primary input voltage |
| --- |
| Get | ZZRV | ; |  |  |  |  |  |  |  |  |
| Answer | ZZRV | P1 | P1 | P1 | P1 |  |  |  |  |  |
| Notes | Read-only; returns nn.n |

| ZZSA Moves VFO A down one Tune Step |
| --- |
| Set | ZZSA | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |
| ZZSB Moves VFO A up one Tune Step |
| Set | ZZSB | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZSD Decrements the Tune Step |
| --- |
| Set | ZZSD | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZSF Sets the variable filter width and center (KD5TFD filters) |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | ZZSF | P1 | P1 | P1 | P1 | P2 | P2 | P2 | P2 | ; |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | P1 = center frequency in Hz. P2 = width in Hz. ZZSF is write-only. |
| ZZSG Moves VFO B down one Tune Step |
| Set | ZZSG | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |
| ZZSH Moves VFO B up one Tune Step |
| Set | ZZSH | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZSM Reads the S-Meter |
| --- |
| Get | ZZSM | P1 | ; |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZSM | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1: 0 = RX1, 1 = RX2 P2 = 000 to 260 Each increment of ZZSM is approximately equal to 0.5 dBm. |

| ZZSO Sets or reads the Squelch on/off status |
| --- |
| Get | ZZSO | ; |  |  |  |  |  |  |  |  |
| Set | ZZSO | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZSO | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZSP Sets or reads the VFO Split (SPLT) status |
| --- |
| Get | ZZSP | ; |  |  |  |  |  |  |  |  |
| Set | ZZSP | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZSP | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZSQ Sets or reads the Squelch control |
| --- |
| Get | ZZSQ | ; |  |  |  |  |  |  |  |  |
| Set | ZZSQ | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZSQ | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 000 to 160. |

| ZZSR Sets or reads the Spur Reduction button status |
| --- |
| Get | ZZSR | ; |  |  |  |  |  |  |  |  |
| Set | ZZSR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZSR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZSS Stops CWX sending (immediate) |
| --- |
| Set | ZZSS | ; |  |  |  |  |  |  |  |  |
| Notes | Write only |

| ZZST Reads the frequency step size |
| --- |
| Get | ZZST | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZST | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 values are expressed in BCD powers of 10 except for non-decade frequencies: 0000 = 10e0 = 1 Hz 0001 = 10e1 = 10 Hz 1000 = special default for 50 Hz 0010 = 10e2 = 100 Hz 1001 = special default for 250 Hz 1010 = special default for 500 Hz 0011 = 10e3 = 1 kHz 1011 = special default for 5 kHz 1100 = special default for 9 kHz 0100 = 10e4 = 10 kHz 0101 = 10e5 = 100 kHz 0110 = 10e6 = 1 MHz 0111 = 10e7 = 10 MHz ZZST is read-only. |

| ZZSU Increments the Tune Step |
| --- |
| Set | ZZSU | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only |

| ZZSW Sets or reads the VFO A TX/VFO B TX Buttons |
| --- |
| Get | ZZSW | ; |  |  |  |  |  |  |  |  |
| Set | ZZSW | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZSW | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 set VFO A to TX, 1 sets VFO B to TX. ZZSW transmits status if Kenwood AI enabled. |

| ZZTF Sets or reads the Show TX Filter checkbox status |
| --- |
| Get | ZZTF | ; |  |  |  |  |  |  |  |  |
| Set | ZZTF | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZTF | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for disabled, 1 for enabled. |

| ZZTH Sets or reads the TX Filter High setting |
| --- |
| Get | ZZTH | ; |  |  |  |  |  |  |  |  |
| Set | ZZTH | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Answer | ZZTH | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Notes | P1 = 00500 to 20000. |

| ZZTI Transmit Inhibit |
| --- |
| Set | ZZTI | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 1 = Transmit Inhibited, 0 = Transmit Enabled. You must follow a ZZTI1 with a ZZTI0 to re-enable the transmitter. |
| ZZTL Sets or reads the TX Filter Low setting |
| Get | ZZTL | ; |  |  |  |  |  |  |  |  |
| Set | ZZTL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZTL | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 0000 to 2000. |

| ZZTO Sets or reads the TUN power setting |
| --- |
| Get | ZZTO | ; |  |  |  |  |  |  |  |  |
| Set | ZZTO | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZTO | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 000 to 100. |

| ZZTP Sets or reads the Transmit Profile |
| --- |
| Get | ZZTP | ; |  |  |  |  |  |  |  |  |
| Set | ZZTP | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZTP | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1: 0 = Conventional 1 = DX/Contest 2 = ESSB 3 = AM Above only correct if no custom profiles saved. P1 is equal to the index value of the profile name in the Transmit Profile drop down list. |

| ZZTS Reads the FLEX5000 Temperature Sensor |
| --- |
| Get | ZZTU | ; |  |  |  |  |  |  |  |  |
| Answer | ZZTU | P1 | P1 | P1 | P1 | P1 | ; |  |  |  |
| Notes | P1 = two places below 100 degrees, one place above 100 degrees: 28.92 or 103.1. |

| ZZTU Sets or reads the Tune (TUN) status |
| --- |
| Get | ZZTU | ; |  |  |  |  |  |  |  |  |
| Set | ZZTU | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZTU | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. Console power must be on for TUN to function. |

| ZZTX Sets or reads the MOX button status |
| --- |
| Get | ZZTX | ; |  |  |  |  |  |  |  |  |
| Set | ZZTX | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZTX | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZUA Reads the XVTR Band Button Names |
| --- |
| Get | ZZUA | ; |  |  |  |  |  |  |  |  |
| Answer | ZZUA | P1 | P1 | P1 | P1 | P1 | P2 | P2 | P2 | P2 |
|  | P2 | P3 | P3 | P3 | P3 | P3 | P4 | P4 | P4 | P4 |
|  | P4 | P5 | P5 | P5 | P5 | P5 | P6 | P6 | P6 | P6 |
|  | P6 | P7 | P7 | P7 | P7 | P7 | P8 | P8 | P8 | P8 |
|  | P8 | P9 | P9 | P9 | P9 | P9 | P10 | P10 | P10 | P10 |
|  | P10 | P11 | P11 | P11 | P11 | P11 | P12 | P12 | P12 | P12 |
|  | P12 | P13 | P13 | P13 | P13 | P13 | P14 | P14 | P14 | P14 |
|  | P14 | ; |  |  |  |  |  |  |  |  |
| Notes | P1 thru P14 equal exactly 70 character spaces and must contain either an ASCII character or a space. Each group of five characters contains the name of the corresponding n-1 XVTR button name: P1 = button 0. |

| ZZVA Sets or reads the VAC button status |
| --- |
| Get | ZZVA | ; |  |  |  |  |  |  |  |  |
| Set | ZZVA | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVA | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZVB Sets or reads the VAC RX Gain |
| --- |
| Get | ZZVB | ; |  |  |  |  |  |  |  |  |
| Set | ZZVB | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZVB | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = -40 to +20 (positive values must lead with sign or “0” |

| ZZVC Sets or reads the VAC TX Gain |
| --- |
| Get | ZZVC | ; |  |  |  |  |  |  |  |  |
| Set | ZZVC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZVC | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = -40 TO +20 (positive value must lead with sign or “0” |

| ZZVD Sets or reads the VAC Sample Rate |
| --- |
| Get | ZZVD | ; |  |  |  |  |  |  |  |  |
| Set | ZZVD | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVD | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 : 0 = 6000 1 = 8000 2 = 11025 3 = 12000 4 = 24000 5 = 22050 6 = 44100 7 = 48000 |
| ZZVE Sets or reads the VOX button status |
| Get | ZZVE | ; |  |  |  |  |  |  |  |  |
| Set | ZZVE | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVE | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZVF Sets or reads the VAC Stereo button status |
| --- |
| Get | ZZVF | ; |  |  |  |  |  |  |  |  |
| Set | ZZVF | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVF | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZVG Sets or reads the VOX Gain value |
| --- |
| Get | ZZVG | ; |  |  |  |  |  |  |  |  |
| Set | ZZVG | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Answer | ZZVG | P1 | P1 | P1 | P1 | ; |  |  |  |  |
| Notes | P1 = 0000 to 1000. |

| ZZVH Sets or reads the I/Q TO VAC Checkbox |
| --- |
| Get | ZZVH | ; |  |  |  |  |  |  |  |  |
| Set | ZZVH | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVH | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZVI Sets or reads the VAC Input Cable |
| --- |
| Get | ZZVI | ; |  |  |  |  |  |  |  |  |
| Set | ZZVI | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZVI | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = 00 to 99, actual input cable depends on VAC driver selected |

| ZZVL Sets or reads the VFO Lock status |
| --- |
| Get | ZZVL | ; |  |  |  |  |  |  |  |  |
| Set | ZZVL | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZVL | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for off, 1 for on. |

| ZZVM Sets or reads the VAC Driver |
| --- |
| Get | ZZVM | ; |  |  |  |  |  |  |  |  |
| Set | ZZVM | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZVM | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = 00 to 99. When you change driver you must reset the I/O cables |

| ZZVN Reads the PowerSDR software version number |
| --- |
| Get | ZZVN | ; |  |  |  |  |  |  |  |  |
| Set |  |  |  |  |  |  |  |  |  |  |
| Answer | ZZVN | P1 | ; |  |  |  |  |  |  |  |
| Notes | Returns ZZVN001.3.14.0; ten total characters including decimal points. |

| ZZVO Sets or reads the VAC Output Cable |
| --- |
| Get | ZZVO | ; |  |  |  |  |  |  |  |  |
| Set | ZZVO | P1 | P1 | ; |  |  |  |  |  |  |
| Answer | ZZVO | P1 | P1 | ; |  |  |  |  |  |  |
| Notes | P1 = 00 to 99, actual output cable depends on VAC driver selected |

| ZZVS Sets the VFO Swap status |
| --- |
| Get |  |  |  |  |  |  |  |  |  |  |
| Set | ZZVS | P1 | ; |  |  |  |  |  |  |  |
| Answer |  |  |  |  |  |  |  |  |  |  |
| Notes | P1 values: 0 = A>B 1 = A<B 2 = A<>B ZZVS is write-only. |

| ZZWA Sets or reads the Mixer Mic Level |
| --- |
| Get | ZZWA | ; |  |  |  |  |  |  |  |  |
| Set | ZZWA | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | ZZWA | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = +000 to -128 |

| ZZWB Sets or reads the Mixer Line In RCA Level |
| --- |
| Get | ZZWB | ; |  |  |  |  |  |  |  |  |
| Set | ZZWB | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | ZZWB | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = +000 to -128 |

| ZZWC Sets or reads the Mixer Line In Phono Level |
| --- |
| Get | ZZWC | ; |  |  |  |  |  |  |  |  |
| Set | ZZWC | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | ZZWC | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = +000 to -128 |

| ZZWD Sets or reads the Mixer Line In DB9 Level |
| --- |
| Get | ZZWD | ; |  |  |  |  |  |  |  |  |
| Set | ZZWD | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Answer | ZZWD | P1 | P2 | P2 | P2 | ; |  |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = +000 to -128 |

| ZZWE Sets or reads the Mixer Mic Select Checkbox |
| --- |
| Get | ZZWE | ; |  |  |  |  |  |  |  |  |
| Set | ZZWE | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWE | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWF Sets or reads the Mixer Line In RCA Select Checkbox |
| --- |
| Get | ZZWF | ; |  |  |  |  |  |  |  |  |
| Set | ZZWF | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWF | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWG Sets or reads the Mixer Line In Phono Select Checkbox |
| --- |
| Get | ZZWG | ; |  |  |  |  |  |  |  |  |
| Set | ZZWG | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWG | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWH Sets or reads the Mixer Line In DB9 Select Checkbox |
| --- |
| Get | ZZWH | ; |  |  |  |  |  |  |  |  |
| Set | ZZWH | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWH | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWJ Sets or reads the Mixer Input Mute All Button |
| --- |
| Get | ZZWJ | ; |  |  |  |  |  |  |  |  |
| Set | ZZWJ | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWJ | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWK Sets or reads the Mixer Internal Speaker Level |
| --- |
| Get | ZZWK | ; |  |  |  |  |  |  |  |  |
| Set | ZZWK | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZWK | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 128 TO 255 Only valid with FLEX5000C + |

| ZZWL Sets or reads the Mixer External Speaker Level |
| --- |
| Get | ZZWL | ; |  |  |  |  |  |  |  |  |
| Set | ZZWL | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZWL | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 128 TO 255 |

| ZZWM Sets or reads the Mixer Headphone Level |
| --- |
| Get | ZZWM | ; |  |  |  |  |  |  |  |  |
| Set | ZZWM | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZWM | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 128 TO 255 |

| ZZWN Sets or reads the Mixer Line Out RCA Level |
| --- |
| Get | ZZWN | ; |  |  |  |  |  |  |  |  |
| Set | ZZWN | P1 | P1 | P1 | ; |  |  |  |  |  |
| Answer | ZZWN | P1 | P1 | P1 | ; |  |  |  |  |  |
| Notes | P1 = 128 TO 255 |

| ZZWO Sets or reads the Mixer Internal Speaker Select Checkbox |
| --- |
| Get | ZZWO | ; |  |  |  |  |  |  |  |  |
| Set | ZZWO | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWO | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. Only valid with FLEX5000C + |

| ZZWP Sets or reads the Mixer External Speaker Select Checkbox |
| --- |
| Get | ZZWP | ; |  |  |  |  |  |  |  |  |
| Set | ZZWP | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWP | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWQ Sets or reads the Mixer Headphone Select Checkbox |
| --- |
| Get | ZZWQ | ; |  |  |  |  |  |  |  |  |
| Set | ZZWQ | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWQ | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWR Sets or reads the Mixer Line Out RCA Select Checkbox |
| --- |
| Get | ZZWR | ; |  |  |  |  |  |  |  |  |
| Set | ZZWR | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWR | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZWS Sets or reads the Mixer Output Mute All Button |
| --- |
| Get | ZZWS | ; |  |  |  |  |  |  |  |  |
| Set | ZZWS | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZWS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZXC Clears the XIT frequency (XIT[0]) |
| --- |
| Set | ZZXC | ; |  |  |  |  |  |  |  |  |
| Notes | ZZXC is write-only. |

| ZZXF Sets or reads the XIT frequency |
| --- |
| Get | ZZXF | ; |  |  |  |  |  |  |  |  |
| Set | ZZXF | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Answer | ZZXF | P1 | P2 | P2 | P2 | P2 | ; |  |  |  |
| Notes | P1 = polarity (+ or -) P2 = frequency in Hz. |

| ZZXS Sets or reads the XIT enable button |
| --- |
| Get | ZZXS | ; |  |  |  |  |  |  |  |  |
| Set | ZZXS | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZXS | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1: 0 = Off, 1 = On. |

| ZZXT Sets or reads the External Control (X2TR) button status |
| --- |
| Get | ZZXT | ; |  |  |  |  |  |  |  |  |
| Set | ZZXT | P1 | ; |  |  |  |  |  |  |  |
| Answer | ZZXT | P1 | ; |  |  |  |  |  |  |  |
| Notes | P1 = 0 for OFF, 1 for ON. |

| ZZZB Clicks the Zero Beat (0 Beat) button |
| --- |
| Set | ZZZB | ; |  |  |  |  |  |  |  |  |
| Notes | Write-only. |

FLEXRADIO CAT COMMAND REVISION RECORD

January 3, 2006 Revisions:

Corrected typo in MD.

Changed ZZMD to reflect DIGU and DIGL.

Added ZZTH and ZZTL commands.

February 25, 2007 Revisions

Added DN and UP commands.

Added special codes in ZZST for new console step size frequencies.

Corrected various typos.

March 20, 2007 Revisions:

Added:		ZZAR		AGC RF GAIN

ZZBR		BCI REJECTION

ZZCB		BREAK IN ENABLE

ZZCD		BREAK IN DELAY

ZZCF		SHOW CW TX FREQ

ZZCI		IAMBIC ON/OFF

ZZCM		CW MONITOR ON/OFF

ZZCT		COMPANDER THRESHOLD VALUE

ZZGE		NOISE GATE ENABLE BUTTON

ZZGL		NOISE GATE LEVEL VALUE

ZZSR		SPUR REDUCTION ON/OFF

ZZTF		SHOW TX FILTER

ZZVA		VAC ON/OFF

ZZVE		VOX ENABLE

ZZVG		VOX GAIN VALUE

ZZXT		X2TR ON/OFF

Updated:	ZZFI (DSP Rx Filters) to reflect current console values.

(Dictionary update only, no change to CAT code).

April 4, 2007 Revisions:

Updated:	GT		AGC Gain

ZZIU		Filter Slider

ZZMT		TX Meter Functions

Obsolete:	FW		DSP Filter Width

August 25, 2007 Revisions:

Updated	MD		Added MD9 for DigU

Added		KY		Send Morse

KS		Get/Set Morse speed

September 16, 2007 Changes:

Updated	     GT		Added 005 for “Custom”

ZZIF		Removed P1 to match IF

ZZMT	Added new meter functions

ZZPA	Added FLEX5000 values

ZZVS	Added IF -> V

Added:

ZZBD	Moves the bandswitch down one band

ZZBU	Moves the bandswitch up one band

ZZER	Sets or reads the RXEQ button status

ZZET	Sets or reads the TXEQ button status

ZZFA	Sets or reads VFO A

ZZFB	Sets or reads VFO B

ZZKS	Sets or reads CWX CW speed

ZZKY	Sends text to CWX for conversion to Morse

ZZMG	Sets or reads the Mic gain

ZZMO	Sets or reads the Monitor (MON) button status

ZZMS	Sets or reads the MultiRX swap checkbox status

ZZMT	Sets or reads the TX Meter mode

ZZMU	Sets or reads the MultiRX button status

ZZNA	Sets or reads Noise Blanker 1 button status

ZZNT	Sets or reads the Auto Notch Filter button status

ZZPC	Sets or reads the Drive level

ZZPD	Sets the Display Pan Center button

ZZPK	Sets or reads the Compressor (COMP) button status

ZZPL	Sets or reads the Compressor Threshold

ZZPA	Sets or reads the Preamp gain

ZZPO	Sets or reads the Display Peak button status

ZZPS	Sets or reads the Power button status

ZZPZ	Sets or reads the Display Zoom buttons

ZZQS	Saves the quick save memory value

ZZRC	Clears the RIT frequency

ZZRT	Sets or reads the RIT button status

ZZSA	Moves VFO A down one Tune Step

ZZSB	Moves VFO A up one Tune Step

ZZSD	Moves the mouse wheel tuning step down

ZZSU	Moves the mouse wheel tuning step up

ZZTP	Sets or reads the TX Profile

ZZTX	Sets or reads the MOX button status

ZZXS	Sets or reads the XIT button status

ZZZB	Zero beats the current signal

September 26, 2007 Changes:

Added		ZZFH		Set TX Filter High

ZZFL		Set TX Filter Low

Corrected minor typos.

October 18, 2007 Changes:

Added		ZZHA		Sets/reads Audio Buffer Size

ZZHR		Sets/reads DSP RX Buffer Size

ZZHT		Sets/reads DSP TX Buffer Size

October 20, 2007 Changes:

Added:		ZZFM		Reads the FlexRadio Model Number.

October 23, 2007 Changes:

Added		ZZEA		Reads or sets the RX EQ

ZZEB		Reads or sets the TX EQ

October 25, 2007 Changes:

Corrected duplicate.  		ZZFL/ZZFH now read DSP Filter Hi/Lo

ZZTL/ZZTH still read TX Filter Hi/Lo

October 31, 2007 Changes:

Added		ZZVB		Reads or sets the VAC RX Gain

ZZVC		Reads or sets the VAC TX Gain

ZZVD		Reads or sets the VAC Sample Rate

ZZVF		Reads or sets the VAC Stereo button

November 21, 2007 Changes:

Added:		ZZUA		Reads the XVTR Band Button Names

Changed:	ZZBS		Added VHF XVTR band buttons to command.

November 29, 2007 Changes:

Added:		ZZOA		Reads or sets the antenna connected to RX1

ZZOB		Reads or sets the antenna connected to RX2

ZZOC		Reads or sets the antenna connected to the transmitter

ZZOD		Reads or sets the current antenna mode

ZZOE		Reads or sets the RX1 Loop

ZZOF		Reads or sets the RCA TX relay jacks

ZZMN		Reads the DSP filter names and values

December 4, 2007 Changes:

Added		AI		Reads or sets the Auto Information function

ZZAI		Same as above

December 12, 2007 Changes:

Modified:	KY		KY1 represents >72 characters in the buffer

ZZKY		Added KY2:  buffer empty and all chars sent

January 16, 2008 Changes:

Added		ZZDX		Sets or reads the Phone DX button status

February 13, 2008 Changes:

Added		ZZWA		Sets or reads the Mixer Mic Level

ZZWB		Sets or reads the Mixer Line In RCA Level

ZZWC		Sets or reads the Mixer Line In Phono Level

ZZWD		Sets or reads the Mixer Line In DB9 Level

ZZWE		Sets or reads the Mixer Mic Select Checkbox

ZZWF		Sets or reads the Mixer Line In RCA Select Checkbox

ZZWG		Sets or reads the Mixer Line In Phono Select Checkbox

ZZWH		Sets or reads the Mixer Line In DB9 Select Checkbox

ZZWJ		Sets or reads the Mixer Input Mute All Button

ZZWK		Sets or reads the Mixer Internal Speaker Level

February 13, 2008 Changes (Con’t)

Added:		ZZWL		Sets or reads the Mixer External Speaker Level

ZZWM	Sets or reads the Mixer Headphone Level

ZZWN		Sets or reads the Mixer Line Out RCA Level

ZZWO		Sets or reads the Mixer Internal Speaker Select Checkbox

ZZWP		Sets or reads the Mixer External Speaker Select Checkbox

ZZWQ		Sets or reads the Mixer Headphone Select Checkbox

ZZWR		Sets or reads the Mixer Line Out RCA Select Checkbox

ZZWS		Sets or reads the Mixer Output Mute All Button

February 15, 2008 Changes:

Obsolete:	PR		Sets or reads the Speech Compressor status

ZZPK		Sets or reads the Speech Compressor status

ZZPL		Sets or reads the Speech Compressor threshold

March 30, 2008 Changes:

Added:		ZZTS		Reads the Flex5000 Temperature Sensor

ZZRA		Sets or reads the RTTY Offset Enable VFO A

ZZRB		Sets or reads the RTTY Offset Enable VFO B

ZZRH		Sets or reads the RTTY DIGH Offset Frequency

ZZRL		Sets or reads the RTTY DIGL Offset Frequency

April 25, 2008 Changes:

Added:		ZZTI		Transmit Enhibit

April 28, 2008 Changes:

Corrected	ZZWA, ZZWB, ZZWC, ZZWD Mixer Input Levels.

July 5, 2008 Changes:

Added:		ZZHU		Reads or sets the DSP Buffer CW RX Size

ZZHV		Reads or sets the DSP Buffer CW TX Size

ZZHW		Reads or sets the DSP Buffer Digital RX Size

ZZHX		Reads or sets the DSP Buffer Digital TX Size

RD		Decrements RIT

RU		Increments RIT

ZZRD		Decrements RIT

ZZRU		Increments RIT

Changed:	ZZHR		Reads or sets the DSP Buffer Phone RX Size

ZZHT		Reads or sets the DSP Buffer Phone TX Size

December 20, 2008 Changes

Corrected	ZZFL		Was: High, Is: Low

Changed:	ZZOA		Reads or sets RX1 Antenna

ZZOB		Reads or sets RX2 Antenna

ZZOC		Reads or sets TX Antenna

Added:		ZZOG		Reads or sets TX Relay Delay Enable

ZZOH		Reads or sets TX Relay Delays

ZZRS		Reads or sets the RX2 Button

January 30, 2008 Changes

Deleted:	ZZPK		Obsolete Speech Processor command

ZZPL		Obsolete Speech Processor command

Added:		ZZFX		Sends FlexWire single data byte command

ZZFY		Sends FlexWire double data byte command

ZZOJ		Reads or sets the Antenna Lock checkbox

ZZTO		Sets or reads TUN Power (missing in Dict. Only)

ZZVH		Sets or reads I/Q to VAC checkbox (missing Dict. Only)

March 20, 2009 Changes

Added:		ZZFV		Reads FlexWire single data byte

ZZFW		Reads FlexWire double data byte

June 19, 2009 Changes

Added:		ZZSS		Stops CWX sending

Modified:	ZZPA		Added FLEX3000

December 23, 2009 Changes

Added 		ZZSW		Reads or sets VFO A TX/VFO B TX Buttons

Modified	ZZSM		Added index “1” for RX2 S-Meter

January 3, 2010 Changes

Added		ZZSM		Added note concerning AI command

January 11, 2010 Changes

Added		ZZSG		Move VFO B one tune step down

ZZSH		Move VFO B one tune step up

February 3, 2010 Changes

Added		ZZVI		Set or read the VAC input cable

ZZVM		Set or read the VAC driver

ZZVO		Set or read the VAC output cable

February 24, 2010 Changes

Added		ZZRV		Reads the primary input voltage

April 1, 2010 Changes

Added 		ZZBY		Closes the console